## Slide 1: Network Programming

## Slide 2: These days almost all devices

## Slide 3: network programming refers to writing programs that execute across multiple devices (computers), in which the devices are all connected to each other using a network. java.net package of the J2SE APIs contains classes for Network Programming. There are two Basic Network protocols, TCP/IP and UDP. Any one of these are required to create network connection between devices.

## Slide 4: TCP: TCP stands for Transmission Control Protocol, which allows for reliable communication between two applications. TCP is typically used over the Internet Protocol, which is referred to as TCP/IP. TCP is Connection oriented Protocol. All packets are traversed thru the connection created between devices. UDP: UDP stands for User Datagram Protocol, a connection-less protocol that allows for packets of data to be transmitted between applications. Packets traverse thru multiple paths, between devices. UDP is not reliable and there is no guarantee in the order of packets received.

## Slide 5
Client
Server
Router
Router
Router
Router
Router
Router

## Slide 6: IP Address: Each device on network is identified by IP Address. Use command ipconfig (windows) ifconfig(Linux) to get ip address of your machine.

## Slide 7
Client Machine
Server Machine
Socket Connection between Client and Server
Socket
port
port
A socket is one endpoint of a two-way communication link between two programs running on the network.
An endpoint is a combination of an IP address and a port number.
Every machine/device on network is identified with IP Address.
127.0.0.1 is Loop back IP Address, which represents current machine, only. Loopback IP Addr is standard across platforms and languages.
Protocol Stack
TCP/IP
Protocol Stack
TCP/IP
Above Client and Server machines are connected with a network
Java Program
Java Program
(listens on a port)

## Slide 8: Data is transferred as packets over sockets. TCP/IP or UDP Protocol stack divide the data (which need to be transferred) into packets.

## Slide 9: A Client is a program, which may or may not run continuously, and sends requests to Server Program, when required. Eg: Web Browser, Whats App client, Skype client, Email client(like outlook),etc... A Server is a program, which is expected to run continously, to provide responses to Client requests. Eg: Web Server, Chat Server, EMail Server. Generally a Server program runs on machine with high hardware configuration, based on number of clients parallely interacting.

## Slide 10
Client Program
Server Program
(listens on a port)
Application Protocols
Socket
port
port
HTTP, HTTPS, SMTP(Simple Mail Transfer Protocol), POP3(Post Office Protocol), FTP(File Transfer Protocol),etc… are Application Protocols, which are further dependent on TCP/IP or UDP underlying Protocols.
Application specific services are provided by Application Protocols
When required, even proprietary Application protocols may be developed. These App protocols, may further depend on TCP/IP or UDP.
TCP/
IP
Above Client and Server machines are connected with a network
UDP
TCP/
IP
UDP
HTTP(s)
SMTP
HTTP(s)
SMTP

## Slide 11: Port Number A device will have multiple(thousands) of Network port numbers. Purpose of port numbers is multiple Network Applications(on a machine) can simultaneously send/receive data. http://www.xyz.com:1234/ Server Standard Port Numbers(for Application Protocols) 80 – HTTP (Protocol used by Web Browser and WebServer) Stands for Hyper Text Transfer Protocol 443 – HTTPS(also used by Web Browser and Web Server, for secured communication) 25 – SMTP(Simple Mail Transfer Protocol) EMails 110 – POP3(Post Office Protocol), Emails FTP- Upload/Download files, SSH –Remote Login

## Slide 12: DNS, Domain Name Server: 1. DNS converts domain name(like www.xyz.com) to corresponding IP address, and vice versa. 2. DNS is required, since a connection cannot be established by directly using domain name, and ip address is required for the same. 3. Domain names are used for convenience of user, and let user to remember website names easily.

## Slide 13
Server
Port 80

## Slide 14
Java.net
Socket
[client & Server]
ServerSocket
[Server only]
TCP/IP
UrlConnection
HttpUrlConnection
DatagramSocket
DatagramPacket
HTTP
UDP
Below are the frequently used classes/interfaces, in network programs
Data is read and written to and from Network Socket using classes/interfaces in java.io package. Hence all Network programs are dependent on java.io package.

## Slide 15: java.net.ServerSocket class is used by server applications to obtain a port and listen for client requests. 1public ServerSocket(int port) throws IOException Attempts to create a server socket bound to the specified port. An exception occurs if the port is already bound(or used) by another application. 2public ServerSocket(int port, int backlog) throws IOException Similar to the previous constructor, the backlog parameter specifies how many incoming clients to store in a wait queue.

## Slide 16: java.net.Socket class represents the socket that both the client and server use to communicate with each other. The client obtains a Socket object by instantiating one, whereas the server obtains a Socket object from the return value of the accept() method. public Socket(String host, int port) throws UnknownHostException, IOException.This method attempts to connect to the specified server at the specified port. If this constructor does not throw an exception, the connection is successful and the client is connected to the server. 2public Socket(InetAddress host, int port) throws IOException This method is identical to the previous constructor, except that the host is denoted by an InetAddress object.

## Slide 17: java.net.Socket class represents the socket that both the client and server use to communicate with each other. The client obtains a Socket object by instantiating one, whereas the server obtains a Socket object from the return value of the accept() method. public Socket(String host, int port) throws UnknownHostException, IOException.This method attempts to connect to the specified server at the specified port. If this constructor does not throw an exception, the connection is successful and the client is connected to the server. 2public Socket(InetAddress host, int port) throws IOExceptionThis method is identical to the previous constructor, except that the host is denoted by an InetAddress object.

## Slide 18: java.net.Socket and ServerSocket uses TCP protocol java.net.DatagramSocket and DatagramPacket uses UDP Protocol Socket programming in Java is also dependent on java.io package. Data is read and written to Sockets using InputStream and OutputStream. Note that connection cannot be directly created using domain name or host name. To create a connection, IP address is required. But IP address is not human friendly, i..e not readable or memorable. Hence DNS(Domain Name Server) converts domain name to IP Address and vice versa.

## Slide 19: Java.net.URLConnection is a interface HTTPURLConnection is an implementation of URLConnection, and is used to send HTTP Request to a Web Server, get and post request

## Slide 20: #1. Simple Client and Server. A Client sends int or float to Server. Server need to multiply with 10, and send result back to Client. Client need to display final value. #2. Develop a console based Server and Client. Client need to send commands like current directory, change directory, list files & file properties(like modified date, etc…). Server program need to provide above details, when requested by client. #3. Implement a simple Web Server, which receives request, and serve the requested file.

## Slide 21: Remote Method Invocation(RMI) RMI is Java specific network protocol, and is used for interaction between two Remote Java objects. Java objects run on different machines which are connected thru network. Hence RMI can be used to develop distributed Java Applications. Internally RMI uses Serialization and Socket Programming. All packages and interfaces required for RMI are available in builtin package java.rmi(which is part of J2SE). Disadvantage of RMI is, RMI cannot be used for interaction between non Java objects.

## Slide 22
Java object1
(on Client)
Machine A
Java object2
(on Server)
Machine B
RMI Network protocol
Interact with remote object
Advantage: No separate Web or Application Server is required
Disadvantage: Only Java remote objects can interact

## Slide 23: Applets: Applets are used to develop GUI(Graphical User Interface) based programming in Java. Below are packages which need to be implemented for Applets java.applet.* java.awt.* Applet LifeCycle

## Slide 24: Swing: Swing is used to develop GUI based programs in Java.Below are advantages of Swing compared to Applet. 1. Swing is light weight compared to Applet. 2. In Swing all UI components are developed fully in Java, but in Applet, native UI Tool kits are used. Hence Swing provides common look and feel across various platforms. 3. Swing provides advanced UI Widgets like Image Button, tabbed panes,etc... Swing UI widgets are in package javax.swing.* package. Event handling in Swing is same as that of Applet, which uses java.awt.event. Now Swing has almost replaced Applets.